## Slide 1: A Magnetometer-Driven Alert System for Asset Protection & Anti-Theft Systems
Submitted by –
Deepti Sahu 25071
Kaniki Bhikshapathi 24489
Puli Suhas Reddy 24123

## Slide 2
# | Use‑Case | What It Detects / When It Fires | Why the Magnetometer + TinyML Approach Matters
1 | Smart Door / Window Tamper Sensor | Lock‑picking, frame prying, or forced entry field spikes | Sees attacks that bypass simple reed‑switch “open/close” contacts
2 | Smart Locker / Safe Monitoring | Drilling, prying, or brute‑force motion near latch | Magnetic tool signature ≠ normal door swing → fewer false alarms
3 | Bike / Vehicle Tampering Alerts | Crow‑bar leverage, grinder motor near frame, or unauthorised movement | Ultra‑low‑power tag works indoors & underground where GPS fails
4 | Catalytic‑Converter Theft Deterrent | Reciprocating‑saw motor and rapid under‑car vibration | Alerts in seconds; signature is hard for thieves to spoof
5 | Container Seal Integrity | Bolt‑cutters, door slam, or magnet used to defeat reed switch | Timestamped BLE packet proves tamper during transit
6 | Museum / Display‑Case Asset Movement | Subtle artifact shift or panel removal | Completely silent & invisible—no privacy or aesthetic issues
7 | Industrial Equipment Protection | Sabotage on control panels, motors, or valves (wrench / drill) | Works in EMI‑heavy plants where vibration sensors chatter
8 | Tamper‑Proof Smart Meters / ATMs | External magnets, drilling, “black‑box” skimming devices | Flags fraud attempts before cash or data is accessed
9 | Indoor Asset Tracking (No GPS) | Movement of tagged tools, racks, or pallets via magnetic “fingerprint” | Reliable localisation in warehouses, basements, ships’ holds
10 | Pipeline Valve Tampering Alert | Wrench actuation or motorised opener at buried valve box | Early warning of sabotage or illegal tapping
11 | Solar‑Panel Theft Deterrent | Sudden unbolting / tilt of ferrous frames | Coin‑cell node + BLE mesh covers remote farms with no mains power
12 | Cargo Door Breach (Trucks / Vans) | Crow‑bar flex or forced unlock different from driver’s key | No line‑of‑sight required; data sent over BLE or mesh instantly
13 | Trailer Hitching Authorisation | Engagement of metallic tongue without permit | Differentiates legitimate hitch from illicit towing
Real-World Use-Cases

## Slide 3
Data Collection and Visualization

## Slide 4
Data Labelling using K-mean Clustering

## Slide 5
Model Training And Performance Analysis
Decision Tree
Random Forest

## Slide 6
Support Vector Machine
Logistic Regression

## Slide 7
LSTM
1D CNN

## Slide 8
GRU – Gated Recurrent Unit

## Slide 9
Model Deployment (Alert System)
Bluetooth enabled system
Open (blinks LED)
Close (No blinking)
We are also tracking the number of counts of change (open to close or vice versa)

## Slide 10
Deep Model Deployment (MLP) using Edge Impulse

## Slide 11
THANK YOU